## Slide 1: Flow-level State Transition as a New Switch Primitive for SDN
Masoud Moshref, Apoorv Bhargava,
Adhip Gupta, Minlan Yu, Ramesh Govindan
(HotSDN’14)
Notes: Today I talk about state machines for SDN switches.

## Slide 2: Motivation
Current practice
Proactive needs a priori knowledge
Reactive has high delay
Opportunity: Local state is enough for many policies (stateful firewall, FTP monitoring, large source IP detection)
Key idea: State machine is a general but efficient abstraction to allow dynamic actions at switches
Notes: Currently, the controller saves flow-based rules in switches in two modes: proactive and reactive.
In the proactive approach, the controller needs a priori knowledge of network events to populate rules in switches ahead of time.
In the reactive approach, switches send events to the controller, but this control loop adds delay and controller overhead.
However, there is an opportunity of reducing the controller involvement as many of the events can be handled by dynamic actions just using the local state at switches.
Thus, our key idea is to use state machine abstraction to allow dynamic actions at switches.

## Slide 3: FAST (Flow-level State Transitions) Abstraction
Examples:
Stateful firewall: TCP state machine with actions that drop uninitiated flows
FTP Monitoring: Track the states of control channel & allow data channel traffic
Large source IP detection: Keep a counter per IP and compare it against a threshold
Controller proactively programs state transitions and actions at switches
Switches run state machines and actions of a state
Notes: We propose FAST, flow-level state transition abstraction at switches.
In FAST, the controller proactively programs state transitions and actions at switches
And then switches update the state machine instances and run actions based on their current state
FAST abstraction is general and can cover many usecases.
For example to implement a stateful firewall, the switch keeps track of TCP state machine and drops packets for uninitiated flows.
In FTP monitoring example, to only allow inbound FTP data channels, we can track states of the controller channel at switches.
And finally, to find large source IPs, we can keep a counter per IP as the state of a state machine and forward packets to the controller if the counter is larger than a threshold.

## Slide 4: FAST Control Plane
None
Init1
Init2
Est
Close1
Close2
SYN
SYNACK
ACK
FIN
FINACK
FAST controller
FAST compiler
Switch agent
Switch agent
Network
Controller translates state machines to switch API
Notes: FAST controller translates state machines to the switch API.
First, the user defines a policy using state machines.
This provides a massive opportunity of debugging and validation.
Then FAST compiles the state machine to make a switch agent per switch.
The switch agent converts the state machine to the switch API and can respond reactively as a backup for not supported features.
Finally it can receive events from the network for network-wide policies

## Slide 5: FAST Data Plane
Match | State machine index
1100** | 0 (UDP)
100*** | 1 (TCP)
Index | State
0 | Est
1 | Init2
2 | Est
Match | State | Action
20.1/16 | None | Drop
10.1/16 | * | Port1
State machine filter
State table
State transition table
Action table
Pick fields and hash
Packet
Packet
Packet, H(p)
Packet, Est
Update state
Packet, Close1
Packet
Match | State | Next state
Fin | Est | Close1
* | Est | Est
Close1
FAST data plane is implementable in hardware switch components
Notes: FAST data plane includes four tables and is implementable using today’s hardware switch components.
First a state machine filter table selects the traffic for a type of state machines. For example for TCP state machines.
Each individual packet corresponds to a state machine instance that may be in a different state, thus we need to find its current state.
The switch hashes the packet and looks up the state table for the current state of an instance.
Then the switch looks for the next state of the state machine in the state transition table.
The table matches on packet fields and the current state that is passed as a metadata with the packet.
The switch saves the next state in the state table and forwards the packet to an action table.
Finally, the action table decides upon the action based on the packet fields and the new state.

## Slide 6: FAST Data Plane Evaluation in Open vSwitch
Delay of going through all TCP states for FAST is small
1 packet, 1 flow : FAST: 28x faster (3ms)
> 64 concurrent flows: 6ms
FAST state lookup has small overhead:
Iperf throughput (Gbps): <5% overhead
Notes: We have implemented FAST in POX and Open vSwitch.
Our experiments with 1 packet flows show that going through all TCP states in FAST is 28 times faster than reactive approach on mininet.
This delay remains small even for many concurrent flows.
On the other extreme, we tested the throughput for a long flow.
As the long flow stays a long time in one TCP state, small throughput reduction shows that the overhead of hashing and state lookup is small.

## Slide 7: FAST Data Plane Evaluation in Open vSwitch
Approach | Mean (ms) | 5th% | 95th%
Proactive | 1.85 | 1.45 | 3.68
Reactive | 84.8 | 57.84 | 109.7
FAST | 3.02 | 1.34 | 5.93
Delay of going through all TCP states for FAST is small
FAST Delay is small even for many concurrent connections
Approach | Mean (Gbps) | STD
Reactive | 8.2 | 0.2
FAST | 7.8 | 0.2
FAST state lookup has small overhead
Flow completion time for TCP connections with 1 data packet
Iperf (large flow) throughput